Histogram Equalizer Unit – Basic design plan

top_without_mem
        Divider
        CDF
     Histogram
Histogram equalizer core
       Top level control

Memory controller

Output memory
Scratch memory
Input memory

Top level structures

1.1	Memory controller (mem_controller.v)

Passes memory interface pins for input and output memories – serving as a wrapper – indicates input memory and output memory full as needed.

Pins	direction	Width	Description
Clock	I	1	Input clock
Reset	I	1	Input reset
histogram_en	I	1	Input from top level FSM indicating if histogram/cdf/divider is enabled. Decides mux of memory interface pins
cdf_en	I	1	Input from top level FSM indicating if histogram/cdf/divider is enabled. Decides mux of memory interface pins
divider_en	I	1	Input from top level FSM indicating if histogram/cdf/divider is enabled. Decides mux of memory interface pins
image_done_pulse	I	1	Input from top level FSM indicating output image has been produced (and reset fault flags)
input_mem_depth	I	17	User programmable input. Indicates size of image that is being processed.
scratch_mem_depth	I	17	User programmable input. Indicates size of image that is being processed.
output_mem_depth	I	17	User programmable input. Indicates size of image that is being processed.
histogram_input_mem_rdata0/1	O	128	Output read data into histogram module from final_input_mem_rdata0/1
histogram_input_mem_raddr0/1	I	16	Input read address from histogram module to be driven into final_input_mem_raddr0/1
histogram_scratch_mem_rdata0/1	O	128	Read data into histogram module from final_scratch_mem_rdata0/1
histogram_scratch_mem_raddr0/1	I	16	Read address from histogram module to be driven into final_scratch_mem_raddr0/1
histogram_scratch_mem_wdata	I	128	Write data from histogram module to be driven into final_scratch_mem_wdata
histogram_scratch_mem_waddr	I	16	Write address from histogram module to be driven into final_scratch_mem_waddr
histogram_scratch_mem_WE	I	1	WE from histogram module to be driven into final_scratch_mem_waddr
cdf_scratch_mem_rdata0/1	O	128	Read data into cdf module from final_scratch_mem_rdata0/1
cdf_scratch_mem_raddr0/1	I	16	Read address from cdf module to be driven into final_scratch_mem_raddr0/1
cdf_scratch_mem_wdata	I	128	Write data from cdf module to be driven into final_scratch_mem_wdata
cdf_scratch_mem_waddr	I	16	Write address from cdf module to be driven into final_scratch_mem_waddr
cdf_scratch_mem_WE	I	1	WE from cdf module to be driven into final_scratch_mem_wdata
divider_input_mem_rdata0/1	O	128	Output read data into divider module from final_input_mem_rdata0/1
divider_input_mem_raddr0/1	I	16	Input read address from divider module to be driven into final_input_mem_raddr0/1
divider_scratch_mem_rdata0/1	O	128	Read data into divider module from final_scratch_mem_rdata0/1
divider_scratch_mem_raddr0/1	I	16	Read address from divider module to be driven into final_scratch_mem_raddr0/1
divider_scratch_mem_wdata	I	128	Write data from divider module to be driven into final_scratch_mem_wdata
divider_scratch_mem_waddr	I	16	Write address from divider module to be driven into final_scratch_mem_waddr
divider_scratch_mem_WE	I	1	WE from divider module to be driven into final_scratch_mem_waddr
divider_output_mem_wdata	I	128	Write data from divider module to be driven into final_output_mem_wdata
divider_output_mem_waddr	I	16	Write address from divider module to be driven into final_output_mem_waddr
divider_output_mem_WE	I	1	WE from divider module to be driven into final_output_mem_waddr
final_input_mem_rdata0/1	I	128	Input from input memory pins with read data0/1
final_input_mem_raddr0/1	O	16	Output to input memory pins with read addr0/1
final_scratch_mem_rdata0/1	I	128	Input from scratch memory pins with read data0/1
final_scratch_mem_raddr0/1	O	16	Output to scratch memory pins with read addr0/1
final_scratch_mem_wdata	O	128	Output to scratch memory pins with write data0/1
final_scratch_mem_waddr	O	16	Output to scratch memory pins with write addr0/1
final_scratch_mem_WE	O	1	Output to scratch memory pins WE
final_output_mem_wdata	O	128	Output to output memory pin with write data
final_output_mem_waddr	O	16	Output to output memory pins with write address
divider_output_mem_WE	I	1	WE output to output memory pins
input_mem_done	O	1	Indicates entire input memory has been parsed
scratch_mem_overflow_fault	O	1	Indicates to scratch memory reader that address pointers are out of range
output_mem_overflow_fault	O	1	Indicates to output memory reader that address pointers are out of range

1.2	Top level FSM (top_level_control.sv)

Port	Direction	Width	Description
Clock	I	1	Input clock
Reset	I	1	Input reset
new_image_pulse	I	1	Input from user indicating new image pulse has been loaded into input memory. 1 clock cycle wide
input_mem_done	I	1	Input from memory controller indicating complete input memory has been read.
scratch_mem_overflow_fault	I	1	Input from memory controller indicating scratch read address pointer is out of bounds – shift state accordingly.
output_mem_overflow_fault	I	1	Input from memory controller indicating output read address pointer is out of bounds – shift state accordingly.
histogram_computation_done	I	1	Input from histogram module indicating histogram calculation has been completed
cdf_done	I	1	Input from cdf module indicating histogram calculation has been completed
divider_done	I	1	Input from divider module indicating histogram calculation has been completed
histogram_start_pulse	O	1	Output to histogram module which triggers start of histogram operations
histogram_en	O	1	Output to memory controller which multiplexes the memory pins to histogram module
cdf_start_pulse	O	1	Output to cdf module which triggers start of histogram operations
cdf_en	O	1	Output to memory controller which multiplexes the memory pins to cdf module
divider_start_pulse	O	1	Output to divider module which triggers start of histogram operations
divider_en	O	1	Output to memory controller which multiplexes the memory pins to divider module
image_done_pulse	O	1	Indicate to user that image processing is complete
input_mem_read_finished	O	1	Indicate to histogram module that all input image pixels have been read.

1.3	Histogram block level

histogram_control

Inputs	Width	Description
Clock	1
Reset
start_histogram	1	From top level control indicating to start histogram. It is 1 clock wide.
input_memory_read_finished	1	From top level control indicating that input memory has been completely read. It is 1 clock wide.
all_pixel_written	1	From data path indicating all pixels are processed and it is ready for a memory read.

Outputs	Width	Description
set_read_address_input_mem	1	Indicate data path to latch input mem address pointer with next value.
set_read_address_scratch_mem	1	Indicate data path to latch scratch mem address pointer with next value.
set_write_address_scratch_mem	1	Indicate data path to latch write mem address pointer with next value.
shift_scratch_mem_rw_address	1	Indicate data path to perform a shift in the rw memory address array to process next pixel.
read_data_ready_input_mem	1	Indicate data path that read data from input memory is ready.
histogram_computation_done	1	Indicate to top level control that histogram computation has been completed.
read_data_ready_scratch_mem	1	Indicate data path that read data from scratch memory is ready.