Histogram Equalizer Unit – Basic design plan

top_without_mem

Divider module
Cdf module
Histogram module
Histogram equalizer core
Top level fsm for pipelined control
Memory controller/ arbiter
Output memory
Scratch memory
Input memory

1.1	Histogram block level

histogram_control

Inputs	Width	Description
Clock	1
Reset
start_histogram	1	From top level control indicating to start histogram. It is 1 clock wide.
input_memory_read_finished	1	From top level control indicating that input memory has been completely read. It is 1 clock wide.
all_pixel_written	1	From data path indicating all pixels are processed and it is ready for a memory read.

Outputs	Width	Description
set_read_address_input_mem	1	Indicate data path to latch input mem address pointer with next value.
set_read_address_scratch_mem	1	Indicate data path to latch scratch mem address pointer with next value.
set_write_address_scratch_mem	1	Indicate data path to latch write mem address pointer with next value.
shift_scratch_mem_rw_address	1	Indicate data path to perform a shift in the rw memory address array to process next pixel.
read_data_ready_input_mem	1	Indicate data path that read data from input memory is ready.
histogram_computation_done	1	Indicate to top level control that histogram computation has been completed.
read_data_ready_scratch_mem	1	Indicate data path that read data from scratch memory is ready.